## Slide 1: Digital Image Correlation
By: Maria Alvarado, Gabriel Kret, and Jonas Margono
Group A2
ME-360: Engineering Experimentation
Spring 2025

## Slide 2: What is a DIC?
Digital Image Correlation (DIC) is a method that measures the deformation and displacement of an object's surface by analyzing the movement of a pattern on its surface captured in a sequence of images.
Notes: Jonas

## Slide 3: Client Need
A robust and repeatable method to experimentally validate linear elastic behavior in beam structures under bending loads.
The setup must accurately capture full-field strain data and allow comparison with theoretical and finite element predictions to ensure model reliability using the Digital Image Correlation rig.
Notes: Gabriel Dr. Wootton franticly came to us with a problem… he needed

## Slide 4
Calipers
Correlated Solutions VIC-EDU Digital Image Correlation System – Included stereo cameras and VIC-Snap/VIC-3D software for full-field strain measurement.
Computer with Python and SolidWorks
Beam Samples – Machined rectangular cross-section beams used as test specimens.
Instron Universal Testing Machine (Model 34TM-50) – Applies controlled compressive loads at the center of the span.
Computer with Instron Software, VIC-Snap 9, and VIC-3D Software
Three-Point Bending Fixture
Calibration Target Plate – Used for camera calibration prior to data collection.
Matte White Spray Paint – Used to add contrast to speckle pattern
Black Speckle Patterning Tool and Ink Pad – Used to create a high-contrast random surface pattern on beam specimens.
Instrumentation
Apparatus
Notes: Maria

## Slide 5: Setup
Instron
Sample with Speckle Pattern
DIC Camera System
Instron Machine
3-Point Bend Rig
Notes: Maria

## Slide 6: Deciding on Sample: Polyurethane vs Aluminum
Pro
High elastic modulus
Con
Not a linear elastic material
Difficulty applying speckle pattern
Cannot assume small strains
Pro
Linear elastic material
Cheaper
Con
Lower elastic modulus
Plasticly deforms under lower loads
Small deflection less DIC resolution
Notes: maria

## Slide 7: Procedure
Apply speckle pattern to spray painted sample
Load the sample onto Instron machine
Calibrate camera system to reduce glare and projection error
Apply loads incrementally, ensuring a picture is captured on the VIC software for each load increment
Analyze data on the VIC software
Extract data for post processing on Python and/or MATLAB
Notes: Jonas Talk about details of calibration procedure too

## Slide 8: Beam Samples
Beam “Name” | Outer Width and Height (in) | Inner Width and Height (in)
Small Solid Beam | 0.625 | N/A
Hollow Box Beam | 0.75 | 0.50
Large Solid Beam | 1.00 | N/A
Notes: Jonas

## Slide 9: Results
Mechanics of Materials
Finite Element Analysis
Digital Image Correlation
Notes: Gabriel –results for aluminum

## Slide 10: Mechanics of Materials
Analytical calculations were conducted using a Python, based on classical Mechanics of Materials theory for simply supported beams under a central load.
Notes: Gabriel
Mechmat Python script is a deliverable, students would use this for their calculations and analysis.
The next few slides are a walkthrough of how the scripts work and the results outputted.

## Slide 11: Elastic or Plastic?
Notes: Gabriel
Part of our stated goal is to be able to test a single sample repeatedly to that end, we need to ensure the beam remains in the elastic range.
Students should Perform a hand-calculation to determine the max load that could be applied before the beam reaches the plastic region.
  Note: The python script includes these calculations and will serve as a check. This value, divided by a factor of safety of 2, will be used as the maximum limit for the force applied by the Instron.

## Slide 12: Deflection
Deflection Along the Length of the Beam for the Small Beam
Peak deflection @ where under a 4000N load
Deflection Along the Length of
the Beam for the Large Beam (
Deflection Along the Length of
the Beam for the Hollow Beam (
Notes: Gabriel
Deflections are lower because the moment of inertia is higher
Symmetric about midspan with maximum deflection at the center.
These values of deflection are very important because of noise in the DIC, as you will see later, the more deflection/movement the easier it is for the DIC to track the speckle pattern, leading to less noise and a more accurate DIC result

## Slide 13: Shear Force and Bending Moments
Notes: Gabriel
Shear: Constant magnitude, switching sign at the centerline
Moment: Linear variation with maximum at midspan
Doesn’t depend on material, only loading conditions

## Slide 14: Analysis at a Specified X value
0.03m
0 m
Support
Load @
0.06 m
0.09 m
0.12 m
Support
Line of Analysis
Notes: Gabriel

## Slide 15: Axial, Lateral, and Shear Strains @ x = 0.09 meters for the Small Beam
Notes: Gabriel
Axial Strain:
  Varies linearly across the beam height.
  Maximum tension at the bottom fiber and maximum compression at the top fiber.
Lateral Strain:
  Induced via Poisson’s effect; compression perpendicular to the applied load.
Shear Strain:
  Parabolic distribution, peaking at the neutral axis and reducing to zero at the outer surfaces.
The corresponding stress fields can be computed by multiplying the Axial and Lateral strains by the Young’s Modulus (E) and the Shear Strain by the Shear Modulus (G)

## Slide 16: 2D Strain Fields: Theoretical Small Beam
Notes: Gabriel
These plots provide a full spatial picture of the mechanical behavior under load, highlighting maximum strains at midspan and diminishing strains near supports.

## Slide 17: DIC Strain Contours Different beams will have different deflections based on size and material properties, How does increased deflection affect DIC results under equal loading conditions?
Small Beam
Large Beam
Hollow Beam
1000N
4000N
Notes: Gabriel

## Slide 18: Finite Element Model
The beams were modeled using SolidWorks with an applied load at half of each beam’s length
Hollow Box Beam
Notes: Maria
Students would make their own model on SolidWorks to compare and then validate the strain fields predicted by the FE model to the strain fields made by DIC

## Slide 19: FE Model: Strain Fields for the Small Beam
Lateral Strain
Axial Strain
Shear Strain
Notes: Maria
Normalized the color bar limits to compare the strain fields to the experimental ones
Axial Strain Analysis
The axial strain field shows a symmetric distribution, with peak tensile and compressive strains concentrated near the points of load application.
The strain values range from -0.0004 to 0.00045, indicating areas of compression near the supports and tension in the mid-span.
This behavior aligns with overall beam bending theory, where the top surface experiences compression and the bottom surface undergoes tension.
Lateral Strain Analysis
The lateral strain is comparatively lower, ranging from -0.00015 to 0.00025.
This suggests the lateral deformation is minimal relative to axial deformation, reinforcing the assumption that bending dominates over lateral expansion or contraction.
Shear Strain Analysis
The shear strain values range from -0.00015 to 0.0001, indicating moderate shear effects.
Shear strain is prominent near the fixed supports, where the beam resists the applied force.
Given the beam’s material (aluminum) and square geometry, this shear strain is expected to be small compared to axial deformation.

## Slide 20: Digital Image Correlation for Small Beam
1000 N:
4000 N:
Notes: Jonas
Show load difference in dic (1000N vs 4000N)
Data was exported from the VIC software and processed using MATLAB to create strain fields for section of the beam within the supports
MATLAB script would be readily available for students to post process data
Axial Strain Comparison
1000 N Case: Strain values range from -1.5 to 1.5 x 10⁻⁴, indicating moderate bending-induced strain distribution.
4000 N Case: Strain values increase to -4 to 4 x 10⁻⁴, revealing a stronger bending effect, aligning with classical beam bending theory.
Higher strain gradients near the loading point and mid-span.
  The regions directly beneath the load application exhibit sharper tensile peaks, with strain values nearly tripling in magnitude.
  Compressive zones near the supports show more concentrated strain, indicating stronger local deformation resistance.
Lateral Strain Comparison
1000 N Case: Strain values range from -2 to 2 x 10⁻⁴, showing minor lateral expansion/contraction.
4000 N Case: The strain range remains similar, implying that lateral deformation is relatively insensitive to load increase.
Unlike axial strain, the lateral strain limits does not significantly increase
However, under 4000N, strain contours expands more noticeably
Shear Strain Comparison
1000 N Case: Values range from -1.5 to 1.5 x 10⁻⁴, with concentration near loading points.
4000 N Case: The shear strain values remain similar, indicating that shear effects are not significantly amplified by the larger force.
At 4000N, there is a clearer concentration of shear strain
Overall Observations
Axial strain is the most responsive to load increase, confirming theoretical bending behavior.
Lateral and shear strain remain relatively stable, aligning with expected material response under three-point bending.

## Slide 21: Small Beam Axial Strain Under 4000N Load
DIC
MechMat
FE Model
Axial Strain cross section
Notes: Jonas
Axial strain fields for the small solid beam under 4000N load:
DIC
The strain distribution captured by DIC reflects the real-world deformation of the aluminum beam under applied loading.
The strain field is slightly asymmetric, possibly due to real-world imperfections in beam geometry, material inconsistencies, or minor misalignments in loading conditions.
FE Model
The Finite Element Analysis (FEA) results show a smoother strain gradient, free from experimental inconsistencies.
MechMat
MechMat theory provides analytical strain predictions based on beam bending mechanics.
Predictions follow the general strain trends observed in both DIC and FE models, though lacking localized effects seen in experimental results.
Overall
DIC occasionally captures higher localized strain due to real-world imperfections that FEA does not account for.
Strain Distribution & Shape:
  FEA and MechMat predict smooth strain transitions, while DIC reveals some irregularities, likely due to material variations and boundary effects.
Agreement on Maximum & Minimum Strain Locations:
All three methods consistently identify peak tensile strain near the beam’s mid-span and peak compressive strain near the supports.
This reinforces classical bending behavior predictions, validating both experimental and theoretical analyses.
Consistent Symmetric Behavior
Despite minor real-world deviations captured by DIC, the strain field across all three methods remains largely symmetric
This symmetry confirms the validity of simulation assumptions and theoretical predictions.

## Slide 22: Large Beam Axial Strain Under 1000N Load
DIC
MechMat
FE Model
Axial Strain cross section
Notes: Jonas/Maria
Larger strain values for the small solid beam compared to the large beam which leads to better results for small beam
Axial strain fields for the small solid beam under 4000N load:
DIC
The strain distribution captured by DIC reflects the real-world deformation of the aluminum beam under applied loading.
The strain field is slightly asymmetric, possibly due to real-world imperfections in beam geometry, material inconsistencies, or minor misalignments in loading conditions.
FE Model
The Finite Element Analysis (FEA) results show a smoother strain gradient, free from experimental inconsistencies.
MechMat
MechMat theory provides analytical strain predictions based on beam bending mechanics.
Predictions follow the general strain trends observed in both DIC and FE models, though lacking localized effects seen in experimental results.
Overall
DIC occasionally captures higher localized strain due to real-world imperfections that FEA does not account for.
Strain Distribution & Shape:
  FEA and MechMat predict smooth strain transitions, while DIC reveals some irregularities, likely due to material variations and boundary effects.
Agreement on Maximum & Minimum Strain Locations:
All three methods consistently identify peak tensile strain near the beam’s mid-span and peak compressive strain near the supports.
This reinforces classical bending behavior predictions, validating both experimental and theoretical analyses.
Consistent Symmetric Behavior
Despite minor real-world deviations captured by DIC, the strain field across all three methods remains largely symmetric
This symmetry confirms the validity of simulation assumptions and theoretical predictions.

## Slide 23: Residual Plots for Hollow, Small and Large Beams
Small
Large
Strain residuals are low
There might be a higher order fit based on residuals above
DIC has trouble analyzing edges of beam therefore residuals are higher toward the outer ranges of the y-axis.
At edges we theorize localized effects, higher residuals
Notes: Jonas

## Slide 24: Lateral Strain for the Small Beam under 4000N Load
DIC
MechMat
FE Model
Notes: Maria
Lateral strain fields for the small solid beam under 4000N load:
All three methods predict minimal lateral strain relative to axial strain
Across DIC, FE analysis, and MechMat thoery, lateral strain magnitudes are significantly lower compared to axial strain (εxx).
This aligns with classical bending theory, confirming that expansion/contraction in the lateral direction is secondary to bending-induced deformation.
Peak lateral strain occurs near load application and edges of beam width
FEA and MechMat theory predict lateral strain concentrations at the beam’s top surface, particularly near the loading point.
The DIC data confirms this, though with small variations in peak strain location due to real-world imperfections.
Similar overall strain field shape across all three methods
DIC, FEA, and MechMat all capture a symmetrical strain distribution about the beam’s centerline.
Strain bands follow the expected lateral expansion/contraction trend, validating theoretical assumptions.
Despite small localized differences, lateral strain patterns remain consistent between experimental, simulation, and theoretical models, supporting their reliability.
All three methods predict similar lateral strain behavior, reinforcing confidence in theoretical models and numerical simulations.
Lateral strain remains significantly lower than axial strain but still following expected trends.

## Slide 25: Shear Strain for the Small Beam under 4000N Load
DIC
MechMat
FE Model
Notes: Jonas
Shear strain fields for the Large solid beam under 4000N load:
Peak Shear Strain
The highest shear strain zones appear along the loading line and near fixed boundary constraints, reinforcing stress concentration areas.
Strain Gradient Transition Matches Across Methods
Despite showing different extents of the beam, all methods capture the same general strain behavior between supports, including a clear transition from tensile to compressive shear strain zones.
Within the supported region, all methods strongly agree on shear strain localization and scaling trends.
The FE model uniquely captures strain distribution beyond the supports, offering full-beam analysis.
DIC provides real-world validation, reinforcing MechMat theory while revealing minor deviations.

## Slide 26: Cross Sectional Shear Strain Plots at x = 30mm
Small Beam
Large Beam
Hollow Beam
Plot shape is an agreement with MechMat theory
Strains are on the same order of magnitude as MechMat theory
Notes: Jonas

## Slide 27: MechMat vs FE Model vs DIC
DIC
MechMat
FE Model
Notes: Maria
Summary of the strain fields for the small solid beam under 4000N
FEA results serve as a reliable validation tool, offering smoother predictions that align well with experimental data.
MechMat theory successfully estimates strain trends, though lacking finer localized details.
The FE model assumes perfectly homogeneous material properties and ideal boundary conditions, which may slightly differ from the experimental results.
Overall, DIC confirms the theoretical predictions but provides additional insight into real-world irregularities.

## Slide 28: Conclusion
We designed a robust and repeatable method to experimentally validate linear elastic behavior in beam structures under bending loads.
The smaller the beam and the larger the force (i.e. the more deflection you’re able to achieve) the better resolution of the DIC results.
With the MechMat Python script, post processing scripts, and FE Model, future students will be able to replicate the experiment for their own learning.
Notes: Maria
Larger deflections/strains introduce
Our setup and procedure accurately capture full-field strain data that has been validated against Theory and Finite Element Methods.
Even though the smaller beam had less speckle pattern, this trade off was shown to be worth it
Although the amount of speckle pattern applied can only go so low..

## Slide 29: We Learned …
Patience and precision matter, small errors can affect the whole process.
Learning to compare and integrate theory, simulation, and real data to validate models critically.
The value of hands-on testing for understanding theoretical concepts.
Learning a completely new technology:
  Precise beam preparation (painting, speckling) is critical for reliable DIC results.
  Misaligned cameras or poor calibration can significantly distort strain data.
  Applying loads too quickly or capturing images during movement can ruin data sets.
Notes: Gabriel
Importance of clear planning and consistent documentation
How to work effectively as a team and divide responsibilities
Communicating frequently prevented confusion, especially during post-processing
Documentation takes time but pays off — clear records made analysis and revisions easier